## Slide 1: Graphene & Nanowires: Applications
Kevin Babb & Petar Petrov
Physics 141A Presentation
March 5, 2013

## Slide 2: What is a Nanowire?
“One-dimensional” structure
  Diameter: 1-100 nanometers (10-9 m)
  Length: microns (10-6 m)
Exhibits crystal structure
  Unlike quantum “dots” (0-dimensional)
Many different materials
  Metals, semiconductors, oxides
Notes: Thin human hair: 100 microns
Mouse embryonic stem cell, silicon array
GaN single wire
ZnO array
Si array
(all SEM)
First, the diameter puts the radial dimension of these structures at or below the characteristic length scale of various interesting and fundamental solid state phenomena: the exciton Bohr radius, wavelength of light, phonon mean free path, critical size of magnetic domains, exciton diffusion length, and others

## Slide 3: Features of Nanowires
Smallest dimension which can transport charge carriers (e-, h+)
  Can act as both nanoscale devices and wiring
  Unique density of states
Controlled synthesis
  Diameter, length, composition
  Electronic structure (band gap, doping)
Size
  Quantum confinement
    Present in some, absent in others
    Unique magnetic & electronic properties
  Millions more transistors per microprocessor
  Probe microscopic systems (e.g. cells)

## Slide 4: Graphene Reminder
Graphene is a 2-d from of pure carbon
Band gap depends on structure
  Large area monolayers
  Bilayers
  Nanoribbons

## Slide 5: Solar Cells
Currently: silicon wafers, thin films
Application of graphene:
  Transparent conducting electrodes
    Robust, conductive, abundant
    Cheaper than ITO
Application of nanowires:
  Enhanced light trapping
  Efficient charge transport (1D)
Notes: Graphene:
http://pubs.acs.org/doi/pdf/10.1021/nl303920b
Shottky junction (metal-semiconductor): light passes through the transparent graphene film to the silicon layer, where it induces the formation of electron–hole pairs. These charge pairs then separate, with the electrons moving toward the silicon, and the holes toward the graphene.

## Slide 6: Graphene-Nanowire Solar Cells
A new design:
  Layer of graphene (transparent cathode)
  Conductive polymer (maintains integrity)
  ZnO nanowire layer (electron transport)
  PbS quantum dots (hole transport)
  Au layer (anode)
Efficiency approaches ITO-based solar cells
  4.2% conversion efficiency (5.1% for ITO)
  Cheaper to produce
Notes: Charge separation: electrons travel up to graphene, holes travel down

## Slide 7: Field Effect Transistors
Challenges to scaling
  Lower transconductance
  Manufacturing difficulties
  Quantum effects
  Gate capacitance
Notes: http://www.nature.com/nnano/journal/v5/n7/fig_tab/nnano.2010.89_F1.html

## Slide 8: Graphene FETs
Challenges
  Low on-off ratios
  High graphene-electrode contact resistance
  Tradeoff between mobility and bandgap
Advantages
  High room temperature mobility
  Thinner than traditional MOSFETs
Notes: http://newscenter.lbl.gov/news-releases/2009/06/10/graphene-bandgap/

## Slide 9: Nanowire FETs
Advantages
  Many different nanowires with different properties
  High mobility
  “Bottom up” synthesis
Challenges
  Integrating NW into circuit
  Control of growth and dopants
Notes: http://cmliris.harvard.edu/assets/IEEETransED_55-2859_Lu.pdf

## Slide 10: Light-Emitting Diodes
LEDs versus conventional lighting:
  Efficient: less heat, lower power consumption
  Long lifetime
  Cheap
  No mercury
How nanowires help:
  Various geometries of p-n junctions available
    Coaxial wires
    Thin film/wire combinations
    Crossed-wire junction arrays
  Unique carrier transport properties
    Natural waveguiding cavities
      Improve extraction efficiency of light
    High surface area improves conductivity
Notes: Marvell Nanofabrication Laboratory (5th floor, Sutardja Dai Hall)
p-GaN (3.43 eV) thin film, vertical n-ZnO (3.37eV) array
Direct band gap needed for radiative recombination
Lots of reflection due to much higher refractive index in semiconductor medium
http://www.cchem.berkeley.edu/pdygrp/pub_files/pubpdf/170.pdf
http://pubs.acs.org/doi/pdf/10.1021/jp051813i

## Slide 11: Artificial Photosynthesis
Simulate natural photosynthetic process
  Convert CO2 and H2O into fuels, O2
    H2O oxidation
    CO2 reduction
How nanowires help: photoelectrodes
  High surface area for reaction sites
  High charge mobility due to small diameter
  Can be grown in large quantities
Notes: http://nanowires.berkeley.edu/wp-content/uploads/2013/01/211.pdf
http://pubs.acs.org/doi/pdf/10.1021/nl100665r
http://www.cchem.berkeley.edu/pdygrp/pub_files/pubpdf/216.pdf
coating n-doped Si wire arrays with n-type InGaN nanowires and annealing the ensemble at high temperatures
Can add lots of catalysts to the InGaN
Photocurrent density 5x higher than if on planar Si

## Slide 12: Touch Screen Devices
Graphene is strong, transparent, highly conductive, and cheaper than traditional ITO
Notes: Graphene absorbs less than ITO, which is what is commonly used now.
http://www.nature.com/am/journal/v2/n4/full/am2010103a.html

## Slide 13
Notes: This is how graphene is transferred to a polymer for support for potential use in touchscreens.

## Slide 14: This is scalable!

## Slide 15: Ultracapacitors
Graphene advantages:
  High surface area to weight ratio (2600 m2 /g)
  High conductivity
  Measured specific capacitance 135 F/g
Uses:
  Electric vehicles
  Backup powering
  High power capability
  Cell phones
Notes: http://bucky-central.me.utexas.edu/RuoffsPDFs/179.pdf
http://www.extremetech.com/computing/105343-graphene-improves-lithium-ion-battery-capacity-and-recharge-rate-by-10x
http://bucky-central.me.utexas.edu/RuoffsPDFs/179.pdf

## Slide 16: References
Physical Foundations of Solid State Devices, E. F. Schubert
Y. J. Hwang, et al., Nano Lett., 2012, 12, 1678–1682
A. Hochbaum, Chem. Rev., 2010, 110, 527–546
H. Park, et al., Nano Lett., 2013, 13, 233-239
E. Lai, et al., Nano Res., 2008, 1, 123-128
D. Siburly, et al., J. Phys. Chem, 2005, 109, 15190-15213
F. Schwarz, Nature Nanotechnology, 2010, 5, 487–496
S. Bae, et al., Nature Nanotechnology, 2010, 5, 574–578
M. Stoller, et al., Nano Lett., 2008, 8, 3498–3502
Y. Zhang, et al., Nature, 2009, 459, 820-823